Accordion Shutters - 3 Part Specs

Architectural Specifications

SECTION 10714: EXTERIOR ACCORDION FOLDING SHUTTERS

PART 1 - GENERAL

1.01 SUMMARY

- Section includes exterior accordion folding, side stacking Hurricane/security, Accordion Shutter protection.

1.02 SUBMITTALS

- Product Data: Submit manufacturer’s complete product data for all specified components, including specifications, finish information and installation instructions.

- Shop Drawings: Submit shop drawings showing layout, sizes and types, product materials, components and accessories, fabrication data, finishes, rough-in dimensions, anchorage and installation requirements and details.

- Samples / colors: Submit minimum six inch length of blade and track section. Include manufacturer’s standard array of color finishes for selection by Architect.

- Quality Assurance Submittals:

  - Certificates: Manufacturer's certification that design criteria meets specified requirements.

  - Operating and Maintenance Instructions: Submit detailed maintenance requirements and operating instructions.

  - Warranty: Submit specified warranty documents.

1.03 QUALITY ASSURANCE

- Installer Qualifications:

  - Use only manufacturer’s factory trained installers or qualified licensed installers approved by shutter manufacturer.

- Regulatory Requirements:

  - Comply with all local and governing code requirements.

  - Unless required otherwise, fabricate to withstand wind loads that carry same rating as component and cladding of walls.

- Pre-Installation Conference: Conduct a pre-installation meeting to verify project installation and coordination requirements, field conditions, and manufacturer instructions.

1.04 DELIVERY, STORAGE AND HANDLING

- Deliver components in manufacturer’s original, unopened, undamaged containers with identification labels intact. Store components protected from harmful weather conditions and damage from other construction activity.

1.05 PROJECT CONDITIONS

- Field Measurements: Verify actual measurements of openings by field measurements before fabrication. Show recorded measurements on shop drawings.

1.06 WARRANTY

- Manufacturer’s Warranty: Submit, for Owner’s acceptance, manufacturer’s standard warranty document executed by an authorized company official.

  - Warranty period: ______________years.

(Specifier Note: Refer to manufacturer’s product data and / or consult with manufacturer’s representative for warranty information / requirements).

PART 2 - PRODUCTS

(Specifier Note: Typically in the following Articles and paragraphs, where items occur in brackets ( ) select item desired for Project).

2.01 MANUFACTURER

- Roll-a-way
1661 Glenlake Avenue
Itasca, IL 60143
(800)446-2500

2.02 COMPONENTS / MATERIALS

- Shutter System: Provide (Hi-Tech) (Bernardo) shutter system.

- Shutter Operation: Manual.

- Shutter Components:

  - Extruded aluminum components, 6063-T6 alloy. Unless otherwise noted.

  - Screws and fasteners: Type 304 or 316 series stainless steel.

  - Provide all required components as necessary for a complete and properly operating installation for the shutter system selected. Required components Include but are not limited to, louver blades, wall header, ceiling header, sill / adjustable sill adapter, roller assemblies with nylon rollers / nylon bushings, sill blade pins, bolts and locking mechanism.

  - Mounting: (wall mounted) (build-out mounted). (ceiling/floor mounted)

2.03 SHOP FINISH

- Electro Static Applied paint meeting AAMA 2603

- Color: ( White) (Ivory) (Bronze) (Beige) (As selected by Architect).

PART 3 - EXECUTION

3.01 EXAMINATION

- Verify conditions of substrates to determine if acceptable for shutter installation in accordance with manufacturer’s instructions. Correct all unsatisfactory conditions prior to commencing shutter installations.

3.2 INSTALLATION

- Install track and all shutter components to comply with project shop drawings and manufacturer’s written installation requirements.

  - Where metal surfaces are in contact with masonry, concrete or dissimilar metals, protect with manufacturer’s recommended isolation coatings or tape.

- After installation, lubricate, test and adjust shutter components to operate properly and free from distortion.

3.03 CLEANING

- Clean installed components in accordance with manufacturer’s instructions prior to Owner’s acceptance. Properly remove from the site all debris remaining from this installation.

- Inadequate surface cleaning will result in corrosion formation & potential structural damage.

3.4 PROTECTION

- Comply with manufacturer’s recommendations and protect completed shutter installations from damage during remaining construction so as not to void warranty.

END OF SECTION